## Slide 1: The Internet
Example Web Request
Internet Architecture
Protocols
Addressing
Routing

## Slide 2
> www.someplace.faraway.com
> Uniform resource locator (url)
Web browser
http client
http server
GET http://www.someplace.faraway.com/index.html HTTP/1.1
HTTP/1.1 202 Accept

## Slide 3
Web browser
http client
http server
TCP
TCP
Connection Handshake
Exchange data

## Slide 4
Web browser
http client
http server
TCP
TCP
IP
IP
IP
IP

## Slide 5
Web browser
http client
http server
TCP
TCP
IP
IP
IP
IP
Frame/Link
Protocol
Link
Prot.
Link
Prot.
Frame/Link
Protocol

## Slide 6
Web browser
http client
http server
TCP
TCP
IP
IP
IP
IP
Frame/Link
Protocol
Link
Prot.
Link
Prot.
Frame/Link
Protocol
Physical
Phy.
Phy.
Physical
01000001
01011010
Internet Architecture

## Slide 7: Internet Architecture
Application Layer
  http, ftp, email, …
Transport Layer
  Program to program communication
  Segment
Network Layer
  End-to-end system communication
  Packet Switching
  Routing
  Packet

## Slide 8: Internet Architecture
Link Layer
  Neighbor-to-neighbor communication
  Frame
Physical Layer
  Bit encoding (how to physically represent a bit)
  Bit

## Slide 9: Protocols
Format and order of messages sent and received
Actions taken when messages are sent and received
Define the way peer layers communicate
Implement services for higher layers based in the services provided by lower layers

## Slide 10: Http Request Message Format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~

## Slide 11: TCP Segment Structure
Source Port Destination Port
Sequence Number
Acknowledgement Number
Hlen Unused Flags Window Size
Checksum Urgent Pointer
Options
Data
32 Bits Wide

## Slide 12: IP v4 Packet Structure
Version Hlen DSCP ECN Total Length
Identification Flags Offset
Time to Live Protocol Header Checksum
Source Address
Destination Address
Options
Data
32 Bits Wide

## Slide 13: Link Layer Frame (802.11)
Frame Cntl Duration ID Addr 1 Addr 2 Addr 3 Sequence Control Addr 4 Data CRC
2 bytes 2 6 6 6 2 6 0-2312 4

## Slide 14: Addressing
Application layer
  Symbolic name
  cps.ce.mu.edu
  Domain name server (DNS)
Transport layer
  IP address + port number
  134.48.24.21:443 (cps.ce.mu.edu)
Network Layer
  IP address
  138.49.101.60 (www.uwlax.edu)

## Slide 15: Addressing
MAC Address (Frame Address)
  0a:1f:a1:02:c6:c2

## Slide 16: Domain Name Server
Distributed database matching names and IP addresses
A Hierarchy of Name Servers
  Root names servers
  Top level domain servers for .com, .edu, etc.
  Authoritative name servers for organizations
    For example uwlax.edu or marquette.edu
nslookup
Recently (name, IP) matches are cached

## Slide 17: DNS Message Structure
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)

## Slide 18: Routing
Interdomain routing
  Routing between Autonomous Systems
Intradomain routing
  Routing within an Autonomous System
Forwarding tables
  When a packet arrives at a router use the destination address in the packet to look up the outgoing link in the forwarding table on which the packet should be sent
Routing Algorithms
  Algorithm to build the forwarding table

## Slide 19: Router with 4 outgoing links
Router
1
2
3
4

## Slide 20: Example Forwarding Table
Destination Address | Outgoing Link
A | 4
B | 1
C | 1
D | 3
E | 2
F | 4
… | …

## Slide 21: Building Routing Tables Dijkstra’s Shortest Path Algorithm
A
B
C
D
G
H
F
E
3
3
2
4
2
2
3
2
2
5
7
9
4

## Slide 22: Dijkstra’s Shortest Path Algorithm
In the following let Distance(X) be the best estimate of the distance to X, let weight(A, B) be the weight on the edge from A to B and let Previous(Y) be the node immediately before Y on the path whose distance is the best estimate of the distance to Y
Set Distance(A) to 0
For all other nodes, X, set Distance(X) to infinity
repeat until the distance to all nodes is known
choose a node, Z, marked unknown such that
Distance(Z) is less than Distance(Y) for any Y marked unknown
mark Z as known
for each node, W, adjacent to Z
if Distance (Z) + weight(Z, W) < Distance (W) then
set Distance (W) to Distance (Z) + weight(Z, W)
set Previous(W) to Z

## Slide 23: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | - | -
B | ∞ | - | 
C | ∞ | - | 
D | ∞ | - | 
E | ∞ | - | 
F | ∞ | - | 
G | ∞ | - | 
H | ∞ | - | 

## Slide 24: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | - | A
C | ∞ | - | 
D | ∞ | - | 
E | ∞ | - | 
F | 9 | - | A
G | 4 | - | A
H | ∞ | - | 

## Slide 25: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | X | A
C | 5 | - | B
D | ∞ | - | 
E | ∞ | - | 
F | 8 | - | B
G | 4 | - | A
H | ∞ | - | 

## Slide 26: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | X | A
C | 5 | - | B
D | ∞ | - | 
E | ∞ | - | 
F | 8 | - | B
G | 4 | X | A
H | 6 | - | G

## Slide 27: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | X | A
C | 5 | X | B
D | 8 | - | C
E | ∞ | - | 
F | 7 | - | C
G | 4 | X | A
H | 6 | - | G

## Slide 28: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | X | A
C | 5 | X | B
D | 8 | - | C
E | 8 | - | H
F | 7 | - | C
G | 4 | X | A
H | 6 | X | G

## Slide 29: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | X | A
C | 5 | X | B
D | 8 | - | C
E | 8 | - | H
F | 7 | X | C
G | 4 | X | A
H | 6 | X | G

## Slide 30: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | X | A
C | 5 | X | B
D | 8 | X | C
E | 8 | - | H
F | 7 | X | C
G | 4 | X | A
H | 6 | X | G

## Slide 31: Build the Forwarding Table for A
Node | Distance | Known | Last
A | 0 | X | -
B | 3 | X | A
C | 5 | X | B
D | 8 | X | C
E | 8 | X | H
F | 7 | X | C
G | 4 | X | A
H | 6 | X | G

## Slide 32: Find Paths
Paths can be found in reverse
  A – B
  A – B – C
  A – B – C –D
  A – G – H – E
  A – B – C- F
  A – G
  A – G- H

## Slide 33: Routing
How does each router know what the graph looks like?
There is no central source of information
Link state packets
Broadcasting
  Flooding
Each router periodically broadcasts information about the state of its links
Each router builds a graph from the link state packets it receives